## Slide 1: Midterm semester project presentation
Automated propeller geometry measurement from 3d scanning data
LIS
Supervisors :
S. Steffen
A. Bhaskaran
Author:
P. Maury Laribière

## Slide 2: Introduction
Analysis of the performance of drones is a very active field of research
No automated method
  Wind tunnels
  Blade Elementum Theory needs geometry information
3D scanning technologies
  Greatly developed in past years
Fig.1: Propeller STL file from 3D scanning

## Slide 3: Introduction: state of the art
3D scanning: 5 main techniques
Fig 2: PARSEC parametrization parameters
From Airfoil Parameterization Techniques: A Review,
Nilesh P. Salunke, Juned Ahamad R. A.2, S.A. Channiwala2
Contact
  CMM
Non contact active
  Structured Light
  Time of flight
  Laser triangulation
Non contact passive
  Photogrammetry
Aerofoil parametrizations:
  Bézier
  PARSEC
  Bezier - Parsec
  Sobieczky (with PARSEC)
  Improved Parameter Geometric

## Slide 4: Introduction: goal of the project Automated propeller geometry measurement from 3d scanning data
Reverse engineering aerodynamics of propellers from 3D scanning data
Point cloud processing
  Projections for Xfoil software
  Parameters
Automation of 3D scanning
  Study of procedures
Fig.3: Point cloud of propeller

## Slide 5
STL to CSV
Find equation of planes
To segment file
Extract point in-between each plane
Project point on plane
Regarding upper and lower points
Method: algorithm (done)
Steps :
Fig.4: Segments of propeller
Fig.5: Projections on plane

## Slide 6
Method: algorithm (to be done)
Finish projections
  X-foil software
  Lift and drag characteristics
Find parameters
  Hub radius, blade twist, chord length etc.
Develop process for automation of propeller 3D scanning
  Study procedures
Fig.6: Parameters of propeller from http://wwwaeroforum.blogspot.com/

## Slide 7: Conclusion
  Issue to know how to project (pair of points)
  Using 3D scanning data for reverse engineering is very promising
  Many choices of parametrizations of propellers and scanning methods

## Slide 8: Thank you for your attention