## Slide 1: Midterm semester project presentation
Automated propeller geometry measurement
from 3d scanning data
LIS
Supervisors :
D. Floreano
S. Steffen
A. Bhaskaran
Author:
P. Maury Laribière
Notes: Automation propeller geometry measurement
From 3D scanning data

## Slide 2: Summary :
Fig.1: Propeller STL file
Introduction
  Initial concepts
  Goal of the project
  State of art
Methodology
  Current progress
  Future work
Conclusion
Notes: First, introduce. Give prior info to understand following
Then, Methodology: done until now, and what is left to do

## Slide 3
Fig.2: Geometric parameters of propeller [7]
Introduction: Initial concepts
Geometric parameters of the blade
  Aerofoil
  Chord length
  Tip radius
  Hub radius
  Blade twist
Cross-section
Notes: Project with propellers.
Explain main terms will use for parameters
Aerofoil = cross sectionnal shape of blade

## Slide 4
Introduction: Initial concepts
Blade Element Momentum Theory:
  Cut in segments
  Relative flow angle
  Prediction thrust and torque
   Aerodynamic characteristics
Fig.3: Velocity and force components of a section of propeller blade in BET [8]
Notes: Nowadays drone perf analysis: BEMT.
cuts the propeller down into discrete segments along the radius
Estimate relative flow angle to blade segment WITH law conservation of momentum
 Predict thrust and torques generated by segment (integrate over radius for all propeller)
 Aerodynamic effect of the air flow on propeller performance -- lift and drag normal and parallel to prop
Method to predict performance of drone based on shape of propeller
Axial component of this hydrodynamic force = element thrust
Moment about the propeller axis of the tangential component = element torque.
Resultant velocity:
-include an axial velocity V0
-a rotational velocity V2 which varies up to the blade tip.
Propeller blade will be set at a given geometric pitch angle (alpha),
Local velocity vector will create a flow angle of attack on the section.
The lift and drag of the section can be calculated using standard 2D hydrofoil properties.
The lift and drag components normal to and parallel to the propeller disk can be calculated so that the contribution to the thrust and torque of the complete propeller from this single element can be found.

## Slide 5: Introduction: Goal of the project
Objectif :
Performance
Blade Element Momentum theory
Shape
3D scanning
Problem :
Shape is not given
Fig.4: Point cloud of propeller
Notes: GOAL: create a tool to analyze performance of drone
Usually drone analysis with:
1. Wind tunnels (not practical)
2. BEMT (need shape)  not easily available. Not published by manufacturers
NEED: propeller shape to understand performance of drone
IDEA:
3D scan propeller  obtain point cloud of its surface  compute parameters and aerofoil shape on based  enable to use BEMT

## Slide 6: Introduction: State of the art
1. Contact
2. Non Contact Active
3. Non Contact Passive
CMM [1]
Structured Light [2]
Time of flight [2]
Laser triangulation [2]
Photogrammetry [3]
5 main techniques
Choices for 3D Scanning:
Notes: Need a scanning method to generate point cloud. 5 main techniques to choose from
Contact : CMM: probe physically touches a firmly fixed object at several points and samples the different positions of the surface
Non contact active ----- rely on the emission of radiation or light.
Structured Light: a pattern of light. Measuring deformation of pattern on the object: shape deduced
Time of flight: Laser beam projected onto surface. Collected by a sensor. ToF of laser beam between its emission and reception provides geometrical information
Laser triangulation: Depending on distance object, reflected light falls at angle on receiving element. Determining spot position, distance object-receiver computed
3. Non CP: Photogrammetry: reconstructs a 3D model object from 2D digital pictures taken at different angles (computer vision + computational geometry algo)

## Slide 7: Introduction: State of the art
Fig 5: PARSEC parametrisation parameters [4]
Bézier [4]
Parsec [4]
Bésier – Parsec [4]
Sobieczky (with PARSEC) [5]
Improved Parameter Geometric [6]
Exemple : Parsec parametrisation
Cross section (= aerofoil shape) parametrisation
Notes: Once scanning data, need to know how to parametrize aerofoil
Aerofoil = cross section
Many techniques which uses different features
Bezier: polynomials curves
Parsec parameters -- improved
Less parameters: IPG
Will try which is best to describe aerofoil obtained from point cloud

## Slide 8: Methodology : Algorithm
Until now:
Step 4 : Projection II
From interpolation of both sides
Step 5 :
Aerofoil shape
Step 6 : Xfoil software
Lift and drag characteristics
Step 7 : Parameters
Hub radius, Tip radius
Chord length, Blade twist
Step 1: Pre-processing
STL to CSV
Principal directions
Step 2: File segmentation
Equation of planes
Point segmentation
Step 3: Projection I
From upper or lower side
Current work:
Future:
Notes: 6 main steps overview

## Slide 9: Methodology : Algorithm
Step 1: pre-processing
  STL to CSV
  Principal direction
Fig.6: Main directions

## Slide 10: Methodology : Algorithm
Step 2: File segmentation
  Select blade
  Equation of planes
  Point segmentation
Fig.7: Segments of propeller
Planes

## Slide 11: Methodology : Algorithm
Step 3: Projections
  On cross section
  From upper or lower side
Fig.8: Projections on plane
Cross-section
Notes: Next idea: regression algorithm OR parametrization method presented in SoA for each edge of the aerofoil
Project leading edge of up on leading edge of down

## Slide 12: Methodology : Algorithm
Step 4: Projections
  On cross sections
  Edges interpolation
  Projection
Fig.9: Projections of leading edge
Aerofoil cross-section
Above plan
Below plan
Upper edge
Upper edge
Lower edge
Lower edge
Notes: Next idea: regression algorithm OR parametrization method presented in SoA for each edge of the aerofoil
Project leading edge of up on leading edge of down

## Slide 13: Conclusion
Propeller shape for drone performance analysis
  Pre-processing and segmentation
  Finish projections
  Xfoil and parameters
  If time: process to automate 3D scanning
Notes: To conclude,
Goal: compute interesting parameter and shape information of propeller from 3D scanning data to be able to use BEMT on it
Done.
Still projections
Then Xfoil and parameters
Optionnal: find processes to further automate the 3D scanning of the propeller using examples of tools available on the market

## Slide 14: Thank you for your attention
Cross-section

## Slide 15
References
[1] A.W.L. Yao « Applications of 3D scanning and reverse engineering techniques for quality control of quick response products» Received: 2 October 2003 / Accepted: 27 January 2004 / Published online: 16 June 2004 © Springer-Verlag London Limited 2004
[2] Morteza Daneshmand, Ahmed Helmi, Egils Avots, Fatemeh Noroozi, Fatih Alisinanoglu, Hasan Sait Arslan, Jelena Gorbova, Rain Eric Haamer, Cagri Ozcinar, Gholamreza Anbarjafari. «3D Scanning: A Comprehensive Survey.» arXiv:1801.08863v1 [cs.CV] 24 Jan 2018
[3] Emmanuel P. Baltsavias. « A comparison between photogrammetry and laser scanning» Institute of Geodesy and Photogrammetry, Swiss Federal Institute of Technology, ETH-Hoenggerberg, CH-8093 Zurich, Switzerland Received 22 October 1998; accepted 17 March 1999
[4] Salunke, Nilesh P., Juned Ahamad R. A., and S.A. Channiwala. "Airfoil Parameterization Techniques: A Review." American Journal of Mechanical Engineering2.4 (2014): 99-102.
[5] Ava Shahroki Alireza Jahangirian Airfoil shape parameterization for optimum Navier–Stokes design with genetic algorithm. « Aerospace Science and Technology», Volume 11, septembre 2017
[6] Lu Xiaoqiang Huang Jun Song Lei Li Jing «An improved geometric parameter airfoil parameterization method.« Aerospace Science and Technology, Volume 78, July 2018
[7] from https://i.stack.imgur.com/Wo8E2.jpg
[8] from Ghassemi, H., & Zakerdoost, H. (2017). Ship hull–propeller system optimization based on the multi-objective evolutionary algorithm. Proceedings of the Institution of Mechanical Engineers, Part C: Journal of Mechanical Engineering Science, 231(1), 175–192. https://doi.org/10.1177/0954406215616655

## Slide 16: Gantt Chart